## Slide 1: Temperature/Humidity/Soil Moisture Sensor First Prototype
By: Marla Ebeid
Omar Helmy
Shireen Afify

## Slide 2: Idea Recap
IoT oriented
Our goal is to measure the temperature and humidity in the corridors of the department as well as the Soil moisture level in the plants and display them on the department’s screens.

## Slide 3: Hardware Components (Updated)
ESP-WROOM-32
DS18B20 Sunfounder Temperature Sensor
DHT11 Sunfounder Humiture Sensor
Soil Moisture Sensor AB054
Jumper Wires
10K Resistors
Power Supply (USB to Laptop)
Breadboard
I2C Lcm1602 Screen

## Slide 4: Software Components (Updated)
Arduino IDE
  Libraries for Temperature Sensor
    DallasTemperature
  Libraries for Humidity Sensor
    DHT
    Adafruit Sensor
  Libraries for LCD Screen
    One Wire
    LiquidCrystal_I2C

## Slide 5: Temperature Sensor Connections
DS18B20 | ESP32
GND | GND
VCC | VCC
SIG | 10K resistor in parallel with D4
LCD | ESP32
GND | GND
VCC | VCC
SDA | D21 (GPIO 21)
SCL | D22 (GPIO 22)

## Slide 6: Humidity Sensor Connections
LCD | ESP32
GND | GND
VCC | VCC
SDA | D21 (GPIO 21)
SCL | D22 (GPIO 22)
DHT11 | ESP32
GND | GND
VCC | VCC
SIG | 10K resistor in parallel with D5

## Slide 7: Demo (Temperature)

## Slide 8: Demo (Humidity)

## Slide 9: Second Prototype Plan
Measure Soil Moisture Level
Integrate the three sensors to display the results on the LCD screen
Finalize any remainders

## Slide 10: Finial Design

## Slide 11: Thank you!